## Slide 1: Title slide + image
Processor Design Project
Group 24

## Slide 2: Context: Why AES is needed?

## Slide 3: Advanced Encryption Standard (AES)
    What is AES?
Symmetric block cipher — same key for encryption and decryption
Operates on a 4×4 matrix of bytes called the state (= 128 bits)
Key is expanded into 11 round keys via the key schedule

## Slide 4: Advanced Encryption Standard (AES)
    How does AES work?
    Initial Round Plain text XOR'd with round key 0
    Middle Rounds × 9
SubBytes — Byte substitution via S-box (confusion)
ShiftRows — Cyclic row shifts to spread data across columns
MixColumns — Column mixing over GF(2⁸) (diffusion)
AddRoundKey — XOR with current round key
Final Round (Round 10) Same as middle rounds but no MixColumns

## Slide 5: Advanced Encryption Standard (AES)
    Where is AES used?
HTTPS/TLS — Every secure website visit (banking, shopping) encrypts data using AES
Wi-Fi (WPA2/WPA3) — Your home/office network uses AES to protect wireless traffic
File encryption — BitLocker (Windows), FileVault (Mac) encrypt your hard drive with AES
Cloud storage — Google Drive, Dropbox encrypt stored files using AES-256
VPNs — All major VPN providers (NordVPN, OpenVPN) use AES as their core cipher
USB drives & SSDs — Hardware-encrypted storage uses dedicated AES engines
Smart cards & passports — AES protects biometric data in modern ID documents
IoT devices — Sensors and embedded systems use AES for secure communication

## Slide 6: Baseline software implementation
Pure C implementation — using standard loads, stores, XORs, shifts
Resource | Count
Cycle Count | 61184
LUTs | 4644
Registers | 2163
Muxes | 284

## Slide 7: Baseline Bottlenecks

## Slide 8: How does hardware help?
    Eliminates all the gf_mult inlining (the 186-instruction mix_columns becomes a handful of aes32esmi calls)
    Operates entirely on registers, with no BRAM loads for the S-box or MixColumn
    aes32esmi combines SubBytes + ShiftRows + MixColumns + AddRoundKey into a single hardware instruction that completes in 1 cycle

## Slide 9: Performance after implementation of AES hardware support

## Slide 10: Vulnerabilities to side channel attacks
The Zkne S-box and MixColumns switch a data-dependent number of bits each cycle, so the instantaneous power draw leaks the byte being processed.
Correlation Power Analysis exploits this: correlating measured power against HW(SBOX[pt XOR guess]) makes the correct key guess separate from the other 255. On our unprotected core a key byte falls in about 100 traces.
Countermeasure: Domain-Oriented Masking (DOM). Every secret is split into two random shares that recombine only inside registered DOM-AND gates, so no single wire (and no glitch) correlates with the real value.
Design follows the TU Delft secure-Zkne paper of Kassimi, Aljuffri, Hamdioui and Taouil (2026).

## Slide 11: Compiler Optimizations: Custom LoopUnroll Pass
What was done?
Wrote our own LLVM compiler pass to fully unroll the 9-round AES loop
Calls LLVM's unroll routine directly instead of using a built-in flag
Flattens all 9 rounds into straight line code
Detects the loop by spotting the AES instructions inside it, so it survives inlining

## Slide 12: Compiler Optimizations: Custom LoopUnroll Pass
Why we did it?
The looped version wastes cycles on loop overhead every round (counter, branch, condition check, key pointer reload).
Built in unrolling is cost model driven and often refuses to unroll, especially when optimizing for size.
Wanted full control to force unrolling on exactly the target loop.
Goal was to build the optimization myself, not just flip a compiler switch.

## Slide 13: Compiler Optimizations: Custom LoopUnroll Pass
Results
Brought the software from 6,260 to 4,800 cycles, about 23 percent faster
Same correct ciphertext, guarantees the loop is always fully unrolled
Build | Unroll Method | Cycles | Vs. Baseline
GCC -Os (looped) | none | 6260 | -
GCC -Os + #pragma unroll | Source pragma | 6067 | -3%
GCC -O2 + -funroll-loops | Build-in flag | 5509 | -12%
Clang –Os + Custom pass | AESUnroll | 4800 | -23%

## Slide 14: RTL Optimization: Parallel DOM S-box
What was done?
Added a custom instruction that runs two DOM protected AES S-boxes in parallel
Each instruction now processes two-byte lanes of a column instead of one
Built a new execution unit in the core (two S-boxes side by side) plus decoder and pipeline changes
Software XORs the two halves together to finish each column
Kept the original single S-box path intact as a fallback

## Slide 15: RTL Optimization: Parallel DOM S-box
Why we did it?
The DOM S-box is the real bottleneck: every byte pays a fixed 5 cycle latency and stalls the whole pipeline
The original design did the S-box one byte at a time, so the 16 bytes per round were fully serial
Running two S-boxes at once halves the number of instructions per round
The masking (side channel protection) had to stay fully intact

## Slide 16: RTL Optimization: Parallel DOM S-box
Results
Stage | Cycles | Vs. Original
Original | 6260 | baseline
Custom Unroll Pass | 4800 | 23% faster
Parallel DOM S-box | 4104 | 34% faster
Resource | Count
Cycle Count | 4121
LUTs | 11987
Registers | 10412
Muxes | 289
DSP | 5

## Slide 17: Validation Framework: Simulation-Based Power Analysis
How we proved the masking works, in simulation and on hardware
Power proxy: a SystemVerilog testbench drives plaintexts through the hardware S-box in Vivado xsim and logs the Hamming weight of the captured result register per trace.
One harness, two S-boxes: the same rig runs against the unprotected and the DOM-masked S-box, producing identical CSVs. The only variable is the design, so the before/after is clean.
Two standard attacks, scored in Python (numpy/scipy):
  CPA: recover the key byte by correlating power with HW(SBOX[pt XOR guess]) over all 256 guesses, 20 000 traces.
  TVLA: Welch fixed-vs-random t-test on 40 000 traces; |t| > 4.5 means first-order leakage (ISO/IEC 17825).
Why simulation first: it isolates the register's switching with no analog noise, giving fast feedback in the RTL loop, alongside Rishi's CW305 hardware validation.

## Slide 18: Validation Results: DOM Defeats the Attack
Same rig, same noise (σ = 2.0). The only change is the S-box, and the leakage disappears.
Metric | Unprotected | DOM-masked
CPA true-key rank | 1 / 256 | 35 / 256
CPA top ¦r¦ | 0.58 | 0.022
TVLA max ¦t¦ | 44.0 | 1.4
Crosses ¦t¦ = 4.5? | Yes (9.8x) | No (0.3x)

## Slide 19: Future Work: The Super Instruction
The observation:
Same operation four times
This results in:
Additional execution overhead
Repeated instruction fetch and decode.
Increased instruction count. .
Independent, highly regular pattern.

## Slide 20: The Super Instruction
The Idea:
i) Introduce a super instruction
ii) Replicate AES32/Zkne datapath four times
iii) Execute in parallel within a single instruction.
iv) Combine the results internally
and write back the final 32-bit result.

## Slide 21: The Super Instruction
Architectural Changes
i) Introduced new opcodes and instruction formats
New instruction encoding includes four source registers:
rs4 | rs3 | rs2 | rs1 | rd | opcode
Single instruction to specify all operands
ii) Modified the register file
Added an additional read port.
Allows all operands to be fetched within a single instruction cycle.

## Slide 22: The Super Instruction
iii) Replicated the Zkne hardware four times
Instantiated four AES32/Zkne datapaths.
iv) Added Software support for these super instructions:

## Slide 23: The Super Instruction
Limitations:
i)Haphazard allocation of new opcodes. Might mess with the RISCV convention in the long run
ii) Did not want to modify the register file architecture for just 2 instructions.
iii) Modest benefit, but high overhead (in terms of utilisation).

## Slide 24: Quote
THANK YOU !!